## Slide 1: Teacher Resources: DIY Mood Ring Project
A TI-Innovator Project
for the TI-84 Plus CE or the TI-Nspire CX
Notes: This powerpoint contains additional information helpful to the teacher in planning for the project. There are additional (optional) slides included here, that can be copied/pasted into the Classroom Presentation PPT designed to be shared with students as desired.

## Slide 2: Overview of Teacher Resources
4. Science Background
Additive Color Model
5. Hands outs and Additional Resources
Handouts that maybe helpful to print for students to have on hand.
6. Example Project With Code
Code for TI-84 Plus CE
Electromagnetic spectrum
Code for TI-Nspire CX
Links to explore, for additional background.
Reference websites
1. Project Overview
Overview
2. Preparing for the Project
Tips for Success
3. Process of Engineering Design and Computational Thinking
Problem
Supply List
Image of Completed Project
Pacing Guide
Materials Checklist
Engineering Design process
Computational Thinking
Pseudocode: Planning your Program

## Slide 3: 1. Project Overview

## Slide 4: Mood Rings: How do they work?
Background:
The mood ring was invented by Joshua Reynolds. Mood rings enjoyed fad popularity in the 1970s and are still around today. The stone of the ring changes color, supposedly according to the mood of the wearer. The 'stone' of a mood ring is really a hollow glass shell containing thermotropic liquid crystals. Modern mood rings are made from a flat plastic strip containing liquid crystals that is inserted into the hollow glass and mounted within the bezel of the mood ring.
Notes: Introductory mini-project for feedback and control systems. The project includes external inputs (temperature sensor), decision logic based on the temperature sensor reading and an output (Red-Green-Blue LED).

## Slide 5: Mood Rings: How do they work?
The crystals respond to changes in temperature by twisting in a regular way. The twisting changes their molecular geometry, which alters the wavelengths of light that are reflected from the crystals.
Wavelengths of light are another way of saying color, so when the temperature of the liquid crystals change, so does the color reflected from the stone. Thus, the ring changes color with the hand temperature of the wearer.

## Slide 6: Time to DIY: Digital Mood Ring!
The Design Challenge:
Design and build a digital mood ring using the pipe cleaner that fits snugly on your finger, placement should be similar to any ring worn on the finger. Be sure the flat part of the temperature sensor is touching your skin.
In this project, you will investigate:
temperature measurement using a temperature sensor and then build a digital mood ring that changes the color of the Hub’s Red, Green, and Blue (RGB) light emitting diode (LED) as the temperature your finger changes.
You can even display what mood you are in on your calculator!
Notes: This project is an ideal introduction for students using the TI-Innovator for the first time. The “DIY- Mood Ring” project includes many of the fundamental concepts that are used in feedback and control projects. The project sets the stage for working through the more advanced Pet Car Alarm and Smart Irrigation projects.
Objectives that will be covered:
  Science Concepts: additive color model, electromagnetic spectrum (optional)
  TI-Technology Concepts: TI-Innovator™ overview, connecting TI-Innovator™ to handheld with unit-to-unit cable (connector with B label in the DATA port of the TI-Innovator), Hub menu for creating commands to send to the TI-Innovator™
  Computing Concepts: physical outputs, numeric arguments for commands

## Slide 7: Mood Ring Project Tasks:
Students are acquainted with the Mood Ring project and the graphing calculator platform. Create and execute a program to display “Hello World”.
Students are acquainted with the TI-Innovator Hub. Create and execute a program using COLOR command to display different colors using the Red-Green-Blue LED.
Students create a program that connects an external temperature sensor, reads values from the sensor and then displays values from the sensor. Students use the pipe cleaner to connect the TI-Innovator and temperature sensor to form a “ring.”
Students build on the program from above to use if-then logic to control COLOR outputs based on temperature readings to create a digital mood ring.

## Slide 8: Standards
NGSS 3-D Standards
  MS-PS1-1 Matter and its Interactions
    PS1-A Structure and Properties of Matter- solids may be formed from molecules, or they may be extended structures with repeating subunits (e.g., crystals
  Science and Engineering Practice:
    Developing and using Models
      Develop a model to predict and/or describe a phenomenon
  Crosscutting Concept:
    Within a natural system, the transfer of energy drives the motion of matter
Notes: Other Relevant connections/Discussion
:
The physics of the actual liquid crystal address MS-PS1-1
https://www.youtube.com/watch?v=1yrtW9Licdo
The biology of blood flow and mood is a life science topic. The flight or fight autonomic response.
This is a basic example of an engineering feedback and control system, a fundamental programming structure used in all Hub projects.
It has a crosscutting concept with the human body’s homeostasis system.

## Slide 9: 2. Preparing for the project

## Slide 10: Materials Checklist and Technology Requirements
Temperature Sensor (per student group)
Cellophane tape
Colored pipe cleaners
*1 per student group (sold in packs of 5)
For TI-Nspire, update to OS 4.5
For TI-84 Plus CE, update to OS 5.3
*Hubs should all be updated to vs. 1.3
*** Note: For optimal student engagement, have students work in groups of 2 or 3 for this project. If supplies are limited, groups of 4 are permissible, but each student should have their own calculator.
Notes: For more information on the TI-Innovator and accessories technology required, visit https://education.ti.com/en/products/micro-controller/ti-innovator?category=accessories

## Slide 11: Project Pacing Guide: Mood Ring
To Extend project beyond 3+ sessions
Project completed in 2-3 sessions
( each lasting 60-90 mins)
Have students complete 10 Minutes of Code and 10 Minutes of Code with Innovator units that have been identified for completion.
Project completed in 1,
60-90 min session
Follow the “Fast Track” Path in the Classroom Presentation PPT
Have students complete all “optional” 10 MOC
This path will likely involve teacher/student working together to create the program (depending on student experience)
Students can customize and create presentations for their rings as time allows
Have students customize and plan multi-faceted presentations for their peers to sell it
Consider the addition of other STEM Projects (refer to last section of this PPT)
Recommended

## Slide 12: Project Tips for Success:
Have students work in teams of 2-3, sharing a TI-Innovator, sensors, etc.
Each student should have a graphing calculator and write their own programs. This enables all students to be actively engaged.
Have additional challenges beyond the main assignment in mind for the students who finish ahead of the others.
When you get to the stage of building the designs, large tables shared by multiple teams can spur discussion and sharing of ideas.
Try to save a few minutes at the end of each session for students or teams to present their designs or programs to the group.
Make sure that students save their programs (and .TNS TI-Nspire files) along the way. Also, whenever possible back up the student’s programs to a computer or another calculator.
We found that students appreciate a certificate of completion for the project. Also, they are proud to share their project at “Techfests” and other events.
Be ready to extend the number of sessions and adapt your agenda based on progress, absences because of other school events, etc.

## Slide 13: 3. Process of Engineering DESIGN and COMPUTATIONAL THINKING

## Slide 14: Engineering Design Process
Define Problem
Design a proposed solution
Present group’s design to class.
Listen to feedback and make appropriate changes.
Build and test the design.
Use test results to make appropriate and informed changes to design.
Present your solution to class.

## Slide 15: Engineering Design Process
Source: Next Generation Science Standards
http://www.nextgenscience.org/sites/default/files/Appendix%20I%20-%20Engineering%20Design%20in%20NGSS%20-%20FINAL_V2.pdf
Defining and delimiting engineering problems involves stating the problem to be solved as clearly as possible in terms of criteria for success, and constraints or limits.
Designing solutions to engineering problems begins with generating a number of different possible solutions, then evaluating potential solutions to see which ones best meet the criteria and constraints of the problem.
Optimizing the design solution involves a process in which solutions are systematically tested and refined and the final design is improved by trading off less important features for those that are more important.
It is important to point out that these component ideas do not always follow in order, any more than do the “steps” of scientific inquiry. At any stage, a problem-solver can redefine the problem or generate new solutions to replace an idea that just isn’t working out.
Authors: NGSS Lead States
Title: Next Generation Science Standards: For States, By States – Engineering Design
Copyright Date: 2013
Notes: Permission received from NGSS.

## Slide 16: Computational Thinking
NGSS Science and Engineering Practices
Using Mathematics and Computational Thinking
http://ngss.nsta.org/Practices.aspx?id=5

## Slide 17: Value of Pseudocode
What is Pseudo code?
Pseudo code is basically written instructions of what a program should do to complete an operation. The pseudo code is written in your speaking language. You simply write down the steps of an algorithm or procedure to make it easier for you or someone else to read it and convert it to a real programming language.
Why was it made/is it used?
It was made to help you specify the steps of a procedure, process or an algorithm without using a programming language. One possible alternative is to use flowcharts.

## Slide 18: Planning your program
Important steps in your program | TI-Basic commands to implement steps in your program
1. | 
2. | 
3. | 
4. | 
5… | 

## Slide 19: Using a flowchart to plan:
Input
Decision Point
Output
Sample, simple flowchart:
Notes: Flowcharts can be helpful tools to think through what the program needs to do.
More about using Flowcharts for planning:
https://www.codeavengers.com/notes/planning/flowcharts
draw.io is a good online tool you can use to create flowcharts. You can logon with a Google Drive account.

## Slide 20: 4. Science Background

## Slide 21
Notes: The human eye has three different types of ‘cones’ on the retina- Red, Blue, and Green. These cones will be activated differently, by different wavelengths of light.
1. All the colors of the visible light spectrum shine on the leaf, but in this case, only light with 520 nm (green light) bounce off.
2. The surface of a green leaf absorbs all of the other colors of the spectrum, except for green, and reflects green to the human eye. Green light reflected stimulates the eye’s cone cells to varying degrees. Which wavelengths are reflected or absorbed depends on the properties of the object.
3. Humans would not be able to see color or objects without LIGHT! Light has to reflect off an object in order to see it.
Different combinations (%) of activation of the 3 types of rods will allow the brain to perceive signals from the retina as different colors. Some estimate that humans are able to distinguish about 10 million colors.

## Slide 22: Background: The Electromagnetic Spectrum

## Slide 23: 5. Student Hand outs and Additional Resources

## Slide 24: Planning your program
Important steps in your program | TI-Basic commands to implement steps in your program
1. | 
2. | 
3. | 
4. | 
5… | 

## Slide 25: Web Resources for additional background info:
Reference on how eyes perceive color
  http://www.cyberphysics.co.uk/topics/light/colorAddition.html
Reference on Color Blindness and Traffic Signals
  https://midimagic.sgc-hosting.com/sigvison.htm
Accessible Pedestrian Signals for the blind
  http://apsguide.org/chapter_overview.cfm
  http://www.apsguide.org/chapter4_walkindication.cfm (includes a WAV file and description of recommended “ticking” sound.)
Use of sensors in traffic control systems
  https://www.youtube.com/watch?v=aMBYXBgxBRs

## Slide 26: TI-Nspire CX Resources:
In addition to the 10 Minutes of Code lesson resources that were used in this project, the following links may be helpful as well:
10 Minutes of Code Teacher’s Lounge (TI-Nspire CX): For a single download of all lessons for 10 Minute of Codes for the TI-Nspire CX in PDF’s:
  https://education.ti.com/en/activities/ti-codes/nspire/teacher-lounge
TI-Innovator Technology eGuide
  https://education.ti.com/html/webhelp/EG_Innovator/EN/index.html
TI-Innovator Hub Commands
  https://education.ti.com/html/webhelp/EG_Innovator/EN/content/eg_innovsys/resources/pdf/ti-innovator_hub_commands_en.pdf
TI-Nspire CX Programming Editor Guide
  https://education.ti.com/html/webhelp/EG_TINspireCode/EN/index.html
YouTube Video (informal, but TI produced) gives you the basics of writing and running TI-Nspire programs that control the TI-Innovator.
  https://www.youtube.com/watch?v=2jjncu8Aba0

## Slide 27: TI-84 Plus CE Resources:
In addition to the 10 Minutes of Code lesson resources that were used in this project, the following links may be helpful as well:
10 Minutes of Code Teacher’s Lounge (TI-84 Plus CE): Select link to download zip files with PDF’s of all of the 10 Minutes of code lessons, teacher and student documents.
  https://education.ti.com/en/activities/ti-codes/84/teacher-lounge
TI-Innovator Technology eGuide
  https://education.ti.com/html/webhelp/EG_Innovator/EN/index.html
TI-Innovator Hub Commands
  https://education.ti.com/html/webhelp/EG_Innovator/EN/content/eg_innovsys/resources/pdf/ti-innovator_hub_commands_en.pdf
TI-84 Plus CE TI-Basic Programming Guide
  https://education.ti.com/html/webhelp/EG_TI84PlusCECode/EN/index.html
TI-84 Plus CE Reference Guide
  https://education.ti.com/html/webhelp/EG_TI84PlusCECode/EN/index.html

## Slide 28: 6. Example Sample programs for completed project

## Slide 29: Example Completed Program- TI 84 Plus CE (Basic code)
Send "CONNECT TEMPERATURE 1 TO IN 1”
“Connect Temperature sensor #1 to Input port #1”
For(C,1,30)
“For loop repeats 30 times”
Send("READ TEMPERATURE 1”)
“Reads the value for Temperature sensor #1”
Get(T)
Disp T
Wait 1
“Gets to variable d then displays the value of T, then Waits 1 second”
If T<26
“Compares values of variable d to determine and show mood”
Then
Send "SET COLOR 255 0 0”
Disp ”MY MOOD IS RED”
End
If T≥26 and T<27
Then
Send "SET COLOR 0 255 0”
Disp ”MY MOOD IS GREEN”
EndIf
If T>27
Then
Send "SET COLOR 0 0 255”
Disp ”MY MOOD IS BLUE”
End
End
Send "SET COLOR 0 0 0”
“Turns the COLOR OFF”
Note: Experiment with temperature values to determine relevant temperature ranges for each person.
TI-84
This program is also available in the MoodRing_Basic.8xv file provided for your reference.

## Slide 30: TI-84 Plus CE- Sample Program (More Advanced Code)
ClrList L₁
ClrList L₂
Send("CONNECT TEMPERATURE 1 TO IN1")
For(N,1,25)
Send("READ TEMPERATURE 1")
Get(T)
Wait 1
Disp "TEMP =",T
If T≤26.6
Then
Send("SET COLOR 0 0 0")
Disp "STRESSED"
End
If T≥26.5 and T≤27
Then
Send("SET COLOR 255 0 0")
Disp "NERVOUS"
End
If T≥27 and T≤27.5
Then
Send("SET COLOR 255 140 0")
Disp "UNSETTLED"
End
If T≥27.5 and T≤28
Then
Send("SET COLOR 0 255 0")
Disp "ACTIVE"
End
If T≥28 and T≤28.5
Then
Send("SET COLOR 0 200 100")
Disp "RELAXED"
End
If T≥28.5 and T≤29
Then
Send("SET COLOR 0 255 255")
Disp "LOVABLE"
End
If T≥29 and T≤29.5
Then
Send("SET COLOR 0 0 255")
Disp "ROMANTIC"
End
If T≥29.5 and T≤30
Then
Send("SET COLOR 255 150 150)
Disp "HAPPY"
End
If T≥30 and T≤31.5
Then
Send("SET COLOR 255 128 0")
Disp "TIRED"
End
If T≥31.5 and T≤32
Then
Send("SET COLOR 255 0 128")
Disp "CALM"
End
T→L₁(1+dim(L₁))
N→L₂(1+dim(L₂))
End
This program is also available in the MoodRing_Advanced.8xv
TI-84
Notes: Students have been presented with extensions, and things to try, and there are always more than one “correct path” when it comes to coding. This is an example of more advanced code that students could generate, or you could share with students after the fact.

## Slide 31: Example Completed Program- TI-Nspire CX (Basic code)
Send "CONNECT TEMPERATURE 1 TO IN 1 ”
© Connect Temperature sensor #1 to Input port #1
For c,1,30
© For loop repeats 30 times
Send "READ TEMPERATURE 1”
© Reads the value for Temperature sensor #1
Get d
Disp d
Wait 1
© Gets to variable d then displays the value of d, then Waits 1 second
If d<26 Then
© Compares values of variable d to determine and show mood
Send "SET COLOR 255 0 0”
Disp "My mood is Red”
EndIf
If d≥26 and d<27 Then
Send "SET COLOR 0 255 0”
Disp "My mood is Green”
EndIf
If d>27 Then
Send "SET COLOR 0 0 255”
Disp "My mood is Blue”
EndIf
EndFor
Send "SET COLOR 0 0 0”
© Turns the COLOR OFF
TI-Nspire CX
This program is also available in the MoodRing_Basic.TNS file provided for your reference.

## Slide 32: TI-Nspire CX – Sample Program (More Advanced Code)
Define mood()=
Prgm
Local t:t:=0
Local n:n:=1
Local t_offset:t_offset:=0
Local key:key:=" "
time:={}
temp:={}
Send "CONNECT TEMPERATURE 1 TO IN 1"
Wait 0.5
For n,1,8
DispAt n,""
EndFor
DispAt 1,"The Mood Ring"
DispAt 8,"Hit Esc key to quit"
For n,1,10
Send "READ TEMPERATURE 1"
Get t
t_offset:=t_offset+t
Wait 0.1
EndFor
t_offset:=((t_offset)/(10))
n:=1
While key≠"esc"
key:=getKey()
Send "READ TEMPERATURE 1“
Get t
DispAt 3,"Temp =",round(t,1),"°C“
If t≥t_offset+9 Then
Send "SET COLOR 0 0 0"
DispAt 4,"STRESSED"
ElseIf t≥t_offset+8 and t<t_offset+9 Then
Send "SET COLOR 255 0 0"
DispAt 4,"NERVOUS“
ElseIf t≥t_offset+7 and t<t_offset+8 Then
Send "SET COLOR 200 85 60"
DispAt 4,"UNSETTLED"
ElseIf t≥t_offset+6 and t<t_offset+7 Then
Send "SET COLOR 0 255 0"
DispAt 4,"ACTIVE"
ElseIf t≥t_offset+5 and t<t_offset+6 Then
Send "SET COLOR 0 0 255"
DispAt 4,"RELAXED"
ElseIf t≥t_offset+4 and t<t_offset+5 Then
Send "SET COLOR 0 255 255"
DispAt 4,"LOVEABLE"
ElseIf t≥t_offset+3 and t<t_offset+4 Then
Send "SET COLOR 64 0 150"
DispAt 4,"ROMANTIC"
ElseIf t≥t_offset+2 and t<t_offset+3 Then
Send "SET COLOR 200 40 255"
DispAt 4,"HAPPY"
ElseIf t≥t_offset+1 and t<t_offset+2 Then
Send "SET COLOR 255 190 0"
DispAt 4,"TIRED"
ElseIf t<t_offset+1 Then
Send "SET COLOR 255 0 255"
DispAt 4,"CALM"
EndIf
Wait 0.5
time[n]:=n*0.5
temp[n]:=t
n:=n+1
EndWhile
EndPrgm
TI-Nspire CX
This program is also available in the MoodRing_Advanced.TNS file provided.
Notes: Students have been presented with extensions, and things to try, and there are always more than one “correct path” when it comes to coding. This is an example of more advanced code that students could generate, or you could share with students after the fact.

## Slide 33: Interested in additional projects or planning a ti STEM camp?

## Slide 34: Suggested Sequence of TI STEM Projects
Mood Ring
simple project designed to introduce students to programming with the TI-Innovator Hub
More complex project, using several sensors at once, and input/output scenarios
Smart Water
requires understanding of more difficult science concepts
time required: 2-3 day project
target audience: general/beginner
time required: ~ .5- 1 day project
target audience: middle grades/High school
target audience: High School
time required: ~ 3-4 days
requires more complex programming and coding skills
heavier emphasis on the E in STEM
Pet Car Alarm
Increasing project complexity, and time required.
Notes: You’ve just completed the Mood Ring! Did your students love it? Are you looking for more, similar projects to help build students coding skills and engagement in STEM Projects? Great news! We have more! The 3 projects listed above are not necessarily dependent on each other, but completing projects in the above order, will ensure students are building their skills, and adding layers on as they progress through the three “core” projects. Also note, that there is some overlap in Student Tasks in the Mood Ring and Pet Car Alarm. If your students have completed both projects, and in the prescribed order, students may be able to skip parts os sections 1-3, as they are nearly identical.

## Slide 35: Choose your own STEM adventure!
Day 1: Coding Basics and Mood Ring
Day 2-2.5/3: Pet Car Alarm
Day 4-5: Mars Rover Challenge
Day 2-4: Smart Irrigation System
Day 4-5: Mars Rover Challenge
Day 3-5: Smart Irrigation System
Day 2-3: Mars Rover Challenge
Addtional On-Ramp to Robotics lessons (availability TBD)
Choose from several recommended combination of projects based on students’ experience and interests!

## Slide 36: Additional Classroom Activities for TI-Innovator Hub can be found online:
Science through Engineering Design Lessons (SED)
  https://education.ti.com/en/tisciencenspired/us/stem/science-through-engineering-design
10 Minutes of Code with TI-Innovator
  https://education.ti.com/en/activities/ti-codes/innovator
Path to STEM Projects
  https://education.ti.com/en/activities/stem/path-to-stem

## Slide 37: Required Supplies for each project - 32 students, groups of 4
 | Mood Ring | Pet Car Alarm | Smart Water | Mars Rover
TI graphing calculators (TI-84 Plus CE or TI-Nspire CX) | 32 | 32 | 32 | 32
TI-Innovators | 8 | 8 | 8 | 8
Input Devices | 8 Temperature sensors | 8 each: Temperature, Hall Effect Magnetic Sensors | 8 Each: Digital Humidity and Temperature, Soil Moisture, Light Level | 
Output Devices or Rovers |  | 8 each: Servo motor (with rechargeable battery) | 8 Each: Pump-MOSFET-Battery Holder kit, 4AA Batteries | 8 Rovers
Other materials | 8 Chenille wires (pipe cleaners) | 8 Cars, magnet, duct tape or other for decoration | Plant container, cistern, perlite or other growing medium, tubes, duct tape | Printouts of Mars surface, plastic obstacle cones, meter sticks, protractors, tape, markers
Notes: For optimal student engagement, groups of 2-3 students would be ideal. We do not recommend having more than 4 students per TI-Innovator set-up. Each student should have their own graphing calculator.