## Slide 1: Mood Ring Project Basics for the Teacher
for TI-Nspire CX OS 4.5

## Slide 2: Digital Mood Ring (introduction to STEM and coding Projects for all levels)
Project Summary:
Bring science and coding together (no coding experience necessary) while developing a mood ring! Explore the science of color mixing while determining the right body temperature thresholds.
This is an excellent first TI-Innovator STEM and coding project. The project includes variables, loops, conditional statements, Boolean operators and other fundamental programming concepts.
Students will complete a series of smaller challenges, as they build the skills needed to complete the final challenge!

## Slide 3: Digital Mood Ring Challenges:
Challenge 1: Use SET COLOR to explore using the color LED. Try to find the RGB values of all the colors in the mood chart.
Challenge 2: Use DispAt command to display your name at several locations on the screen.
Challenge 3: Use a For..EndFor loop to display the numbers 1 through 10.
Challenge 4: Connect a temperature sensor to the TI-Innovator Hub and display the temperature on the calculator.
Challenge 5: Use a loop to read and display temperature.
Challenge 5 Extension (Optional): Use a loop to read, display and log into list arrays for time and temperature. Graph the result.
Challenge 6: Use a While..EndWhile loop along with getKey() command to monitor temperature and make a decision to display a message, “Hot” or “Cold”. Then modify your program to include a 3rd level between hot and cold, “Nice”.
Final Challenge: Build a mood ring to repeatedly read the temperature sensor, determine the mood of the person, display the temperature value and display the mood.

## Slide 4: TI-Nspire CX Resources:
Step-by Step YouTube videos designed for the teacher with a detailed, demonstration of each challenge. The videos are intended to guide those new programming in general, programming on the TI-84 Plus CE and programming with the TI-Innovator Hub.
  https://www.youtube.com/playlist?list=PL17Fe0ZmhCR_j09b202PUI0wfaRYSLQka
10 Minutes of Code Teacher’s Lounge (TI-Nspire CX): For a single download of all lessons for 10 Minute of Codes for the TI-Nspire CX in PDF’s:
  https://education.ti.com/en/activities/ti-codes/nspire/teacher-lounge
TI-Innovator Technology eGuide
  https://education.ti.com/html/webhelp/EG_Innovator/EN/index.html
TI-Innovator Hub Commands
  https://education.ti.com/html/webhelp/EG_Innovator/EN/content/eg_innovsys/resources/pdf/ti-innovator_hub_commands_en.pdf
TI-Nspire CX Programming Editor Guide
  https://education.ti.com/html/webhelp/EG_TINspireCode/EN/index.html
YouTube Video (informal, but TI produced) gives you the basics of writing and running TI-Nspire programs that control the TI-Innovator.
  https://www.youtube.com/watch?v=2jjncu8Aba0

## Slide 5: Quick Code Reference:
for TI-Nspire CX OS 4.5

## Slide 6: Background: Input/Output Commands for Displaying and Requesting text strings and numeric values
Disp "hello world”
Disp 2+3
Request "Input a number",n
Disp n
RequestStr "Input a string”,s
Disp s
Display a string
Display a numeric value
Request a numeric value input
Prompt
Variable for the input numeric value
Request a string input
Program Editor Input/Output Menu
Prompt
Variable for the input text string

## Slide 7: Background: For Loop
Control variable
Ending Value
Program Editor Control Menu
Initial Value
For c,1,3
© Insert code to be repeated
EndFor

## Slide 8: Background: Decision Making and Logic Statements
If b>10 Then
© set of commands executed if statement is true
EndIf
If-Then command
If b>10 Then
© set of commands executed if statement is true
Else
© set of commands executed if statement is false
EndIf
If-Then-Else command
If b>10 and c>100 Then
© set of commands executed if both statements are true
EndIf
“and”
If b>10 or c>100 Then
© set of commands executed if either of the statements
EndIf
“or”
Logic functions
Decision Making Commands
Note: Relational operators can be found on the keyboard using [=] and ctrl [=]. Logic functions, and, or, not, etc. can be typed or found in the catalog.

## Slide 9: Background: While…EndWhile loop
The While loop repeats a set of commands as long as the While condition is true.
Command Syntax:
While condition
Commands in While block
EndWhile
b:=1
While b>.25
Send "READ BRIGHTNESS ”
Get b
Disp b
EndWhile
Note: This program uses the BRIGHTNESS sensor as a control for the While loop. If you completely cover the sensor the While loop will stop.

## Slide 10: Background: Advanced Version Storing Data in an Array
Declare an array variable
Inside a loop store a calculation or Store a value from a sensor
myarray:={}
For c,1,3
myarray[c]:=c*2:
EndFor
myarray:={}
For c,1,3
Send "READ BRIGHTNESS ”
Get b
myarray[c]:=b
EndFor
Values can be plotted on a data and statistics page, graphs page, or used in other calculations.

## Slide 11: Background: Advanced Version Ending a loop using a keypress
Initialize default value.
Continually set the value of keys pressed.
Local key:key:=“ "
While key≠"esc“
key:=getKey():
© set of commands executed while escape key isn’t pressed
EndWhile

## Slide 12: Background: Basics of programming with the TI-Nspire CX.

## Slide 13: Create a new document
Press [Home] key
Select New Document from home menu

## Slide 14
Important Keys
esc: Gets you out of what you are in
Ctrl z: is undo, just like on a computer
On: (House): Brings you to the Home screen (see next slide)
ctrl: Allows you to access the blue label functions printed above the keys.
Var: gives you a list of variables, including programs to choose from to insert in your command.
Menu: Gives you a list of commands that are relevant for your current application.
touchpad: is like a mousepad, slide your finger around. Center click when finger icon is showing to select. You can also click the arrows to move the cursor space-by-space.
enter: Completes and entry or selects a menu item or closes a dialogue box.
doc: has file commands. Save for example.
Ctrl doc (+page) : adds a new page

## Slide 15: Home Menu
New Document: create a new document file.
My Documents: Brings you to folders with your stored files.
Current: Returns you to the document that you have open.

## Slide 16: Set up a new Program Editor page as a place to run the programs that we write

## Slide 17: Program Editor Page
Remember to move cursor DOWN within the program

## Slide 18: Store your program
Use the Check Syntax & Store Menu to store your program. Look for the “stored successfully” message.
Use Run to store and automatically paste the program name on a Calculator page, ready for execution.
Make sure the title says “stored successfully”

## Slide 19: Insert a calculator page to run your program
You can move from page to page by pressing ctrl-LEFT arrow and ctrl-RIGHT arrow
or by using the touchpad to move the pointer to the desired page then click the center of the touchpad or press ENTER

## Slide 20: Execute your program
1. Select the program name from the [var] menu.
2. Press [enter] to execute the program.
3. “Done” indicates that the program is finished.

## Slide 21: Save the TI-Nspire document with your program
3. Select 5: Save As…
Press the [doc] key
2. Select 1:File Menu

## Slide 22: Save the TI-Nspire document with your program
1. Select a Folder with the touchpad and click
2. Type in your file name - Press [enter] to save.
Ctrl-S is a shortcut to save a file with the current name.
KTXJ8296
KTXJ8296

## Slide 23: Completed Project Sample Code:

## Slide 24: Background: Example Program (Basic)
Send "CONNECT TEMPERATURE 1 TO IN 1”
© Connect Temperature sensor #1 to Input port #1
For c,1,30
© For loop repeats 30 times
Send "READ TEMPERATURE 1”
© Reads the value for Temperature sensor #1
Get d
Disp d
Wait 1
© Gets to variable d then displays the value of d, then Waits 1 second
If d<26 Then
© Compares values of variable d to determine and show mood
Send "SET COLOR 255 0 0”
Disp "My mood is Red”
EndIf
If d≥26 and d<27 Then
Send "SET COLOR 0 255 0”
Disp "My mood is Green”
EndIf
If d>27 Then
Send "SET COLOR 0 0 255”
Disp "My mood is Blue”
EndIf
EndFor
Send "SET COLOR 0 0 0”
© Turns the COLOR OFF
Additional Challenges
Add more than three moods.
Replace the For loop with a While loop that allows the user to stop the sampling process.
Note: Experiment with temperature values to determine relevant temperature ranges for each person.

## Slide 25: Background: Example Program (Advanced)
Send "CONNECT TEMPERATURE 1 TO IN 1”
time:= { }
temp:={ }
n = 0
Local key:key:=“ "
While key≠"esc“
key:=getKey():
© loop repeats until the escape key is pressed
Send "READ TEMPERATURE 1”
Get d
Disp d
time[n]:=n
temp[n]:=d
n := n + 1
Wait 1
If d<26 Then
Send "SET COLOR 255 0 0”
Disp "My mood is Red”
EndIf
If d≥26 and d<27 Then
Send "SET COLOR 0 255 0”
Disp "My mood is Green”
EndIf
If d>27 Then
Send "SET COLOR 0 0 255”
Disp "My mood is Blue”
EndIf
EndWhile
Send "SET COLOR 0 0 0”
Additional Code
Stores the temperature values and the time to list variables. This data can be displayed on a plot of time vs. temperature on another page after the loop is done.
For loop was replaced with a While loop that allows the user to stop the sampling process.
Initialize Arrays
Store Data
While loop controlled by keys pressed