## Slide 1: Meet the TI-Rover with Geometry Challenges TI-Nspire CX Family TI-Basic
Texas Instruments
@ticalculators
www.TIstemProjects.com
Contact stem-team@ti.com with questions

## Slide 2: Meet the TI-Innovator™ Rover

## Slide 3
TI-Innovator™ Rover
TI-Innovator™ Hub
TI Graphing Calculator

## Slide 4: Rover from the top
Battery indicator
Red-Green-Blue (RGB) Color LED
On/Off Switch
Marker holder
(Expo Fine and
Ultra Fine sizes)
Calculator holder posts.
Lift and twist to CE or CX side.
Battery Charge with USB micro to wall adapter.

## Slide 5: Turn Rover Over
What do you see?

## Slide 6: Sensors on Rover
Motors to turn the wheels
Ranger to measure distance
Color sensor to detect different colors

## Slide 7: TI-Rover orientation and virtual grid
Rover programs set the initial position as the origin and the heading as 0 degrees measured from the x-axis.
Note: The Rover tracks its position on a virtual coordinate grid with a unit value of 10 cm. The coordinate grid position applies to the RV TO XY, RV TO POLAR, and RV TO ANGLE on the Drive RV Drive menu. The virtual grid also applies to the RV Path menu functions.

## Slide 8: Connecting Rover to your calculator
Plug B side into USB B port of the Rover Hub.
Unit-to-unit cable
Plug A side into port on calculator the Rover Hub.
Make sure that your Rover is switched on and
on floor ready to roll before running the program.
3
1
2

## Slide 9: Connecting your calculator to the Rover
Initial Connection
Step 1: Make sure that Rover is switched ON
Step 2: plug unit-to-unit cable into Hub
  (Use end of cable labeled B)
Step 3: plug unit-to-unit cable into the calculator
  (Use end of cable labeled A)
Troubleshooting
Try the following as a fast fix:
Step 1: unplug the unit-to-unit cable from the hub and the calculator.
Step 2: re-connect in the order of first Hub then calculator second.
If the fast fix does not work, try these steps:
Step 1: unplug unit-to-unit cable from both the hub and the calculator
Step 2: Switch Rover OFF
Wait a second
Step 3: Switch Rover ON
Step 4: plug unit-to-unit cable into Hub
Step 5: plug unit-to-unit cable into the calculator

## Slide 10: Creating a new TI-Nspire document
Press the [home/on] key to
display the home screen.
Use arrow keys and [enter] or
Press [1] to select 1 New document.
See next slide for steps to add
a program.
1
2
3

## Slide 11: Creating a Rover Program
Note: You can also add a new page
to the document by pressing
[ctlr] [doc] +page.
Press [menu] to bring up a menu
of applications to add to the page.
Press down arrow repeatedly then press [enter] or
press [9] to select Add Program Editor.
Select 1: New by pressing [enter] or [1]
Enter your program name
and press [enter].
You begin on a blank program line.
Press [menu] then [8] Hub [7] Rover (RV) [8] Send “Connect RV”
The Connect RV command
is required at the beginning of every Rover program. Note: Right arrow to the end of the line and press [enter] to complete the statement.
Press [menu] then [8] Hub [7] Rover (RV) [1] Drive RV [1] FORWARD to paste to the edit line. Type a value for units to drive. Right arrow to the end of the line and press [enter] to complete the statement.
Press [ctrl] [R] to run the program in a calculator app on the next page.
1
2
3
4
5
6
7
8

## Slide 12: Running a Rover Program
Press [ctrl] [R] to paste the program name ready to run in a Calculator app on the next page.
Note: [ctrl] [R] also checks syntax and stores program changes. [ctrl] [B] is another option for checking syntax and storing. * before the program name indicates that changes have not been stored.
Before running the program
make sure that
- Rover is connected to the calculator
- Rover is switched on
- Rover is on a flat surface ready to roll
Press [enter] to run your program in the Calculator app.
You can re-run the program in the Calculator app by pressing [enter].
1
2

## Slide 13: Editing a Rover Program
Press [ctrl] left to go back to your editor page.
Use the arrow keys to position the cursor to change the value of the forward distance.
Press [del] to backspace over the 3.
Type in a new value for distance,
right arrow to the end of the line,
then [enter] to move to the next
line.
Press [ctrl] [R] to paste the program name ready to run in a Calculator app on the next page.
1
2
3
4
5
6
Press [enter] to run your program in the Calculator app.

## Slide 14: Saving a TI-Nspire document file
Press [doc] then select 1 File
from the menu by pressing
[enter] or [1].
Select 4 Save or 5 Save As… from the menu.
Type in your file name using alpha and numeric characters.
Note: The name must begin with an alpha character.
Press [enter] to save the file to the
folder indicated above.
To change the folder press the
[UP] arrow key and then use
arrows and [enter] to select a
folder before pressing [enter] to
save the file.
Press [esc] to cancel the save
dialogue.
You can use [ctrl] [S] as a shortcut
to save the TI-Nspire document file.
1
2
3
4
Folder where file will be saved.

## Slide 15: Opening an existing TI-Nspire document file
Press the [home/on] key to
display the home screen.
Use arrow keys and [enter] or
Press [2] to select 2 Browse files.
Use arrow keys and [enter] to select a folder and a file.
Note: Pressing the [home/on] key
repeatedly toggles between the home screen and the current document.
1
2
3

## Slide 16: Drawing with the TI-Rover
Use Expo Fine or Extra Fine dry erase markers.
The markers drop into a slot on the front of the Rover.
Note: The Texas Instruments Workshop Loan Rover cases include markers.
Drawing surface: We recommend butcher paper held in place with painters tape on a hard surface.

## Slide 17: MAKE IT MOVE!
Task: Discover how far Rover drives per unit.
Use differing values (1-20) to determine what 1 Rover unit is.
New Program:
Press [menu] key to see TI-Basic Program Editor options.
Press [ctrl] [R] to paste the program name ready to run in a Calculator app on the next page. Press [enter] in the Calculator app to run the program.
Use [ctrl] left to move from the Calculator page back to the editor page.
Find ”CONNECT RV” on the 8:Hub>7:Rover menu.
Find FORWARD on the 8:Hub>7:Rover>1:Drive RV menu.
Enter value for number of units to drive.
Right arrow to the end of the line and press [enter] to complete the command and move to the next line.
Notes: Explain “Connect RV”
Then demo how to add Send “CONNECT RV” to the first line in the program.
Give students time to explore with different distances to figure out.
Use [ctrl] left and [ctrl] right to move from page to page in the document.

## Slide 18: Set the color
Task: Set the color output of the RGB LED.
Each color takes a value (0-255).
Challenge Task: Try to make Yellow
New Program:
Find RV.COLOR on the 8:Hub>7:Rover>5:RV.Color menu.
Separate the values for Red, Green and Blue with spaces.
.
Press [menu] key to see TI-Basic Program Editor options.
Press [ctrl] [R] to paste the program name ready to run in a Calculator app on the next page. Press [enter] in the Calculator app to run the program.
Use [ctrl] left to move from the Calculator page back to the editor page.
Enter values for Red, Green and Blue separated by spaces.
Notes: Explain import ti_rover module
Then demo how to import and how to enter the statements.
Give time to explore.

## Slide 19: Explore angles
Task: Drive a square.
Challenge Task: Try to drive an equilateral triangle.
New Program:
The program above is a framework for driving a square.
Enter values for distance and turn angle.
Notes: Explain import ti_rover module
Then demo how to import and how to enter the statements.
Give time to explore.

## Slide 20: Quick Math Reminders
Complementary Angles:
  Sum to 90 degrees
Supplementary Angles:
  Sum to 180 degrees

## Slide 21: Quick Math Reminders
Exterior angles:
Interior Angles:

## Slide 22: Logic Challenge
Task: Drive the figure shown without crossing any lines or going back over a line and without picking up the pen.
When you are ready put the pen in and trace your path
Notes: First challenge is to drive the shape without crossing any lines and without picking up the pen.

## Slide 23: Where can you go next with TI-Rover?
Drive an obstacle course
Drive a design
Draw artwork
Park your Rover
Use a For loop
to draw polygons
Write your name
Navigate a map

## Slide 24: Quick Math Reminders
Pythagorean Theorem

## Slide 25: Logic Challenge 2
Task: Drive the figure shown without crossing any lines or going back over a line and without picking up the pen.
When you are ready put the pen in and trace your path
Notes: First challenge is to drive the shape without crossing any lines and without picking up the pen.
Second will be to drive at least one segment in reverse direction.

## Slide 26: Logic Challenge 2
1
2
3
4
5
6
7
8
9
10
Notes: First challenge is to drive the shape without crossing any lines and without picking up the pen.
Second will be to drive at least one segment in reverse direction.

## Slide 27: Thank you!
See www.TIstemProjects.com for more TI STEM and coding activities and projects.